MADLAT   (Unsupported Program)
				======

	This program reads one or more output files from Madnes and
writes a file of vectors representing a weighted reciprocal lattice or dots,
suitable for display in Frodo, using the option Mol>lattice.

	The ideas for this were stolen from Garry Taylor, bits of code
from ABSURD

					Phil Evans  July 1989


Control input
=============

MAXINTEN upper intensity (used for scaling -- should not be too big)
          (may be smaller -- and usually is -- smaller than maximum intensity)

ZONES resrict to zone: may be HK0, H0L, or 0KL

TITLE "title"

	The rest of the line will be printed as comment at the beginning
	of the vector file

RESOLUTION   Dmin Dmax

	Resolution limits in Angstrom, either order. If only one number
	is given, it is treated as the high resolution limit

NUMBER    number_of_reflections

	Set maximum number of reflections displayed. If more than this
	number of reflections are found in all files within the resolution
	limits, they are sorted on resolution, and the first 
	"number_of_reflections" taken

FILE  filename

	Read reflections from Madnes output file. Data from a series
	of files may be combined together by a series of FILE commands

DOTS

	Write reflections as dots instead of octahedrons. This allows
	display of many more reflections to visualize coverage of
	reciprocal space

GO

	Write vector file: this is also done on hitting the end of the
	command stream



Example:
--------

$ madlat vector junk.vec
MAXINTEN 1000
resolution 200 5
number 1000
title Ovalbumin test
file scratch_disk0:[fastuser]ovaldy1_120_001.dat
go