OSCGEN
 
***********************************************************************
Last change to this documentation 28/10/85. Add FILMS keyword. A.G.W.L.
                                  19/11/85  Add FIRSTPACK keyword. A.G.W.L.
                                  19/12/85  Add option of giving a filename
                                            as parameter to MATRIX keyword.
                                   9/ 6/86  Change UNIQUE output LCF logical
                                            filename from LCF12 to HKLOUT.
                                  22/12/86  Add keyword GRAPH to allow
                                            SIGMA or TEKTRONIX graphics
                                  15/2/89   Add keyword FAST to allow
                                            the UNIQUE option to be used
                                            for FAST data collection
                                            strategy.
                                            Expand description of POINT
                                   7/ 3/89  Add PLOT84 Graphics option for
                                            hard copy output.
                                  11/ 5/89  Add SERIAL card for specifying
                                            many packs (from Howard Terry)
                                            Add LNO3 graphics option for
                                            hard copy plots (from Duilio
                                            Cascio)
                                   9/ 8/90  Replace all tabs with spaces.
                                   8/ 1/91  UMAT filename option
                                  21/ 3/91  Optimize the size of the
                                            measurement box using the
                                            spot separation of the
                                            predicted pattern. See
                                            additional documentation in
                                            RASTER, GROW and YHOR.
                                  10/ 9/91  NOGEN option
                                  25/ 9/91  Reflection width calculation
                                            included to allow integration
                                            of reflections spanning 3 images
                                            by MOSFLM
                                  25/10/91  For IP data, intensities stored
                                            as I*4 words
                                  1/6/91    Changed HKLOUT format from LCF
                                            to MTZ. This required a slight
                                            change in the column labels.
***********************************************************************
 
 
Generates list of reflections to be observed on each rotation film.  The spot
prediction algorithm is based on R.M. Sweet's implementation of the algorithm
proposed by G.N. Reeke.
 
 
THIS PROGRAM HAS THREE MODES OF OPERATION:
 
A.
Outputs a file containing a list of reflections and the calculated positions to
be input to a film measurement program. With NOGEN option, only the generate
file header and pack headers are output (no reflections). The reflection list
is generated within MOSFLM. This allows refinement of orientation and cell
parameters within MOSFLM.
 
B.
UNIQUE OPTION
Outputs a file in MTZ format containing a list of generated reflections with
indices reduced to a unique asymmetric unit of reciprocal space.  This file can
be used with the the programs UNIQUE and COMPLETE in order to determine the
percentage of unique data recorded (and the multiplicity of observations)
for a given oscillation range. The data are generated in batches of (say)
5 degree rotations, and COMPLETE will monitor how many unique reflections
are observed as successive 5 degree batches are included. This allows the
user to determine what total rotation range is required to observe any desired
fraction of the unique data. If desired the program can be run more than once
with different crystal orientations (or detector positions for the FAST)
and the resulting MTZ files merged before running into COMPLETE (See
FIRSTPACK keyword)
See UNIQUE.DOC for complete documentation.
 
C.
TESTGEN OPTION
Calculates the number of fully recorded, partial and overlapped reflections
on each film for a given total rotation range and a series of different
oscillation angles. The information may be written to an ouput file to plot
using CURVY.
 
MATRIX AND AXIAL CONVENTIONS
 
The program uses an orthogonal axial system with:
 
        X  along the the X-ray beam (away from source)
        Z  along the spindle axis (away from goniometer)
        Y  completes the right-handed system (upwards)
 
 
A positive rotation is clockwise when viewed along axis away from the origin.
 
The dimensionless reciprocal space vector X is given by:
                                          -
                     
        X  =  [PHI] * [PHIMIS] * [U] * [B] * h
        -                                    -
 
        [PHIMIS] = [PHIMISZ] * [PHIMISY] * [PHIMISX]
 
        [A] = [U] * [B]
 
where
 
        h is the vector h,k,l
        -
 
        [B] is an orthogonalization matrix to convert indices h,k,l to
        cartesian crystal axes x,y,z.
 
        [B] =  ( a*     b* cos gamma*   c* cos beta*            )
               ( 0      b* sin gamma*  -c* sin beta* cos alpha  )
               ( 0           0            lambda / c            )
 
               Ref. W.R.Busing & H.A.Levy, Acta Cryst. (1967) 22, 457-464
 
        This gives x parallel to a* and y in the a* b* plane.
        Here a*, b* and c* are in dimensionless reciprocal lattice units.
 
        [U] is a rotation matrix to define the standard orientation.  It
        rotates the crystal cartesian coordinates (x,y,z) to the camera
        cartesian coordinate frame (X,Y,Z).  [U] is usually a simple permutation
        matrix.
 
        [PHIMIS] is the missetting matrix.
 
The film coordinates are Yf across the film parallel to the crystal Z axis.
Xf is vertical (upwards) parallel to the crystal axis Y.
 
The program input is key-worded using PARSER.  The program only checks the
first 4 characters.  All angles are in degrees and distances in mms.
 
The possible key-words are:
 
CASSETTE        -  type of cassette
CELL            -  crystal cell parameters
CRYSTAL         -  crystal class
DISPERSION      -  wavelength dispersion
DISTANCE        -  crystal to film distance
DIVERGENCE      -  width of the rocking curve or beam divergence if mosaic
                   spread specified separately.
DSTARMAX        -  maximum resolution in dimensionless r.l. units.
FAST            -  filename of the FAST savefile.
FILMS           -  number of films in a pack.
FIRSTPACK       -  pack number of first pack generated in UNIQUE option
GRAPHICS        -  specifies graphics device, Sigma, Tektronix, PLOT84
                   or LNO3 (postscript laserprinter)
GROW            -  increase the size of the measurement box generated by
                   OSCGEN
IDENTIFIER      -  crystal identifier
INTENSITY       -  intensity limit for second and subsequent films in pack
LATTICE         -  lattice type, can be P,A,B,C,I,R,F
LIMITS          -  area on film in which reflections can be measured
MATRIX          -  matrix A
MISSET          -  missetting angles
MOSAIC          -  mosaic spread
NOGEN           -  do not output reflection list, only headers (for use with
                   POSTREF option in MOSFLM for orientation refinement).
PACK            -  number and oscillation range for a given pack
RASTER          -  defines size and shape of reflection measurement box.
                   Atlernatively, it provides the criteria for selecting
                   the measurement box after an analysis of the spot
                   separation of the predicted patterns.
RESOLUTION      -  maximum resolution in Angstrom
PLOT            -  flag for plotting spot positions on the graphics terminal
                   or producing a PLOT84 file for hard copy.
                   When used in conjunction with TESTGEN option, writes a
                   file to FT04 suitable for input to CURVY to give a plot
                   of the number of overlaps vs rotation angle for different
                   oscillation angles.
POINT           -  point group for crystal - required for UNIQUE option only
PRINT           -  print all generated relections - for debugging
SEPARATION      -  minimum separation between reflections on the film
SERIAL          -  allows specification of many abutting packs, as an
                   alternative to many pack cards
SYNCHROTRON     -  synchrotron geometry
TESTGEN         -  test generation of a given total rotation range using
                   different oscillation angles and calculating number of
                   fulls, partials and overlaps on each film. The number
                   of overlaps may be plotted if PLOT option is included.
TITLE           -  to read in title
UMAT            -  matrix U
UNIQUE          -  generates all observed reflections over a given total
                   rotation range in blocks of a specified angular size
                   (ie in different packs). Generates a list of reflections
                   with indices reduced to asymmetric unit, for input
                   (after merging with unique reflection data) to COMPLETE.
                   The crystal point group must be specified using POINT.
WAVELENGTH      -  wavelength
YHOR            -  swap the X- and Y-coordinates of a measurement box
                   generated by OSCGEN
 
 
 
CASSETTE  option
        option = FLAT (default) or VEE
        Only need to specify when using Vee cassettes.
 
CELL x x x x x x
        Cell parameters.  Must be given when specifying U matrix.
 
CRYSTAL x
        Crystal class. One of the following keywords:
                TRIClinic
                MONOclinic
                ORTHorhombic
                TETRagonal
                TRIGonal
                HEXAgonal
                CUBIc
                RHOMbohedral
 
        This sets up the LCELL matrix which contains six flags one for
        each cell parameter:
                -1  for a freely variable parameter
                 0  for a fixed cell parameter
                 I  (I > 0) parameter constrained to have same value
                        as parameter I.
DISPERSION  x
        (delta-lamda)/lamda (default is 2.5E-3 for CuKalpha)
 
DISTANCE x
        Crystal to film distance, or crystal to Vee distance. (mms)
 
DIVERGENCE x [x]
        Horizontal and vertical widths of the rocking curve.  If only
        one number given then vertical divergence set to horizontal value.
        (default is .3 for both)
 
DSTARMAX x
        The maximum resolution in dimensionless r.l. units. (default set by
        maximum radius on film).  The maximum resolution can also be set
        using the RESOLUTION card.  If neither DSTARMAX nor RESOLUTION is
        given then the maximum resolution defaults to that determined by
        maximum radius on the film.
 
FAST   x
        The filename of the FAST savefile. The crystal orientation, cell
        parameters, detector position (distance and swing angle), RMAX,RMIN,
        beam parameters (horizontal and vertical divergence, wavelength
        and dispersion), mosaic spread, resolution and the TITLE are
        read from this file and the identifier is made up from DERI and
        XTAL .
        NOTE WELL that the beam missetting angles mu1 and mu2 and the
        detector angles tau1 and tau3 are all assumed to be zero. Only
        the detector swing angle tau2 is used. Also the detector camera
        constants and pixel limits are ignored.
        The detector is assumed to be 64mm high and 48mm wide, and any
        reflection lying within that area AND not more than 38mm from
        the centre of the detector is considered as observed. In practice
        reflections close to the edges of the detector will be rejected
        by MADNES because of large non-uniformity corrections. This should
        not seriously affect the total number of data measured (I hope).
        The detector size can be modified by the LIMITS keyword if
        desired.
        When using the UNIQUE option the user MUST still supply
        the LATTICE, CRYSTAL and point group (POINT), because although
        this information can be extracted from the space group number I
        can't be bothered to write the code !
        The rotation range should be given on the UNIQUE card (see below).
        For multiple runs with different detector positions the FIRSTPACK
        keyword must also be used.
        All parameters read from the FAST SAVEfile can be overridden by
        using the appropriate keyword.
 
FILMS    x
        The number of films in a pack, required by MOSFLM. Default is 3.
 
FIRSTPACK x
        The pack number of the first pack generated in UNIQUE option. This
        is only required if several OSCGEN runs are required to generate
        data with different crystal orientations. See UNIQUE keyword and
        documentation.
 
GRAPHICS  SIG, TEK (TX), LNO3 or PLOT84
        Specifies graphics device if PLOT option is being used. If
        PLOT84 is given, a PLOT84 file is written to logical file PLOT
        which can be used to get a hard copy of the plot. The PLOT card
        must also be included to get a hard copy plot. LNO3 will produce
        a file suitable for a laserprinter with postscript (also to logical
        file PLOT).
        DEFAULT is TX
 
GROW    x
        A real number defining the increase in size of a measurement
        box generated by OSCGEN. By default, no increase takes place.
        If no new measurement box was generated this card is ignored.
        It might not be a good idea to increase the size of a box
        by more than a factor of 4 (with GROW 2.0 for example), since
        this guarantees during film measurement at least one of the
        boxes will contain more than one spot, even if the camera
        constants and the film distortion parameters are known exactely.
        For additional information  on the generation of measurement
        boxes: see RASTER.
 
IDENTIFIER xxxxxxxx
        Crystal identifier (up to 8 characters).
 
INTENSITY  x
        Reflections with an intensity less than this will not be measured
        on the B and C films. (default is 300)
 
LATTICE    x
        Lattice type, must be one of the following: P,A,B,C,I,R,F
 
LIMITS keywords
        Defines usable area of film.  Several key words can be repeated on
        one line or several limits cards can be specified.
        Possible key-words are:
                                                Defaults
                                         Flat           Vee     FAST
        XMIN x          minimum Xf        0             5.0       0
        XMAX x          maximum Xf        58            82       24
        YMAX x          maximum Yf        58            58       32
        RMIN x          minimum radius    3.5           3.5       0
        RMAX x          maximum radius     *            88       38
                * = MIN(SQRT(XMAX**2+YMAX**2),58)
 
MATRIX x x x x x x x x x
        The A matrix as A11,A12 etc.  Not required if U matrix given.
        If a filename is given here, then the [A] matrix AND the
        missetting angles will be read from that file, format (3F12.6).
        This file can be output from IDXREF by using the
        OUTFILE keyword or from REFIX (written to logical filename MATRIX).
 
MISSET x x x
        The misorientaion angles. (default to zero)
 
MOSAIC x
        Mosaic spread of crystal in degrees.
        Defaults to zero if not specified. For standard source it is
        normally included in divergence.
        Data collected from a variety of crystals at Daresbury suggest
        that a value of 0.05 degrees is typical for a fresh (native)
        crystal. However, to provide some lattitude for errors in the
        cell parameters, orientation angles, and the possibility
        of slight crystal slippage, it is advisable to increase the
        mosaicity by between 0.03 and 0.05 degrees. Note that the
        mosaicity may well increase during data collection due to
        radiation damage. This should be monitored using POSTCHK
        and the mosaicity increased accordingly.
 
NOGEN
        If this card is present, only the generate file header and the pack
        headers are written to generate file, no reflection records are
        written. This is COMPULSORY if the POSTREF option is to be used
        in MOSFLM, which allows post-refinement to refine the crystal
        orientation and (for high symmetry space groups) cell parameters
        from within MOSFLM itself. This is only possible with image plate
        data, as it relies on summing partially recorded reflections over
        adjacent images. All images MUST have the same oscillation angle
        and exposure time for this to work satisfactorily.
 
PACK Packnumber Phibegin Phiend
        One card required for each pack to be generated (max of 200).
        Packnumber - identification number for this pack.
        Phibegin,Phiend - rotation angle for this pack
 
RASTER nxs nys nc nrx nry pixel
        The first five parameters define the spot measurement box.
        The sixth parameter is the scanner increment in microns
        (usually 50).  NXS, NYS (odd integers) define the overall
        dimensions of the rectangular array of optical density points
        for each spot. NRX, NRY are the number of columns or rows
        of points in the background rim and NC the corner background
        cut-off which corresponds to a half-square of side NC points.
        A single boundary line of points between the peak and
        background areas are omitted from calculations.
 
        If NC<0 the corner cut-off is set at !NC! but the corner
        points so defined are ignored; that is not used for peak or
        background. This feature can be useful with spots on a centred
        lattice where the corners of the measurement box are close to
        an adjacent spot.
 
        If NC=0 the pixels in the rectangular corner defined by
        NRX,NRY are omitted from peak and background.
 
        Alternatively, OSCGEN can be instructed to generate a measurement
        box based on an analysis of the separation between the spots of
        the generated pattern. This is done by specifying a zero or
        negative number for NXS and/or NYS. The following strategy is
        adopted:
          For each spot boxes are constructed in such a way that the
          examined spot coincides with the upper or the lower right side
          corner of the box. The opposite corner of the box is located at
          the position of another spot. If no spots are found inside
          such a box, its dimensions are stored, provided that no other
          box with both a smaller height and width already had been stored
          previously.
          If both the height and width of a box are smaller than those
          specified by the SEPARATION card, the spot is flagged as an
          overlap and none of the boxes associated with this spot are
          stored.
 
        The criteria for selecting a box are determined by the actual values
        of NXS and NYS:
        - (NXS .EQ. 0) .AND. (NYS .EQ. 0)
          The box with the largest surface is selected.
        - (NXS .GT. 0) .AND. (NYS .LE. 0)
          From the boxes with a width in pixels of at least NXS, the one
          with the the largest surface is selected. If none of the boxes is
          as wide as NXS, the widest one is selected.
        - (NXS .LE. 0) .AND. (NYS .GT. 0)
          From the boxes with a height in pixels of at least NYS, the one
          with the the largest surface is selected. If none of the boxes is
          as high as NYS, the highest one is selected.
        - (NXS .LE. 0) .AND. (NYS .GT. 0)
          The box with a width to height ratio as close as possible to
          NXS/NYS is selected.
 
        If NXS and/or NYS are zero or negative, the values of NC, NRX and
        NRY take on a slightly different meaning: NRX and NRY are now
        the width and height in pixels of the peak-area, including the rim
        of pixels to be ignored. NC is the corner-cutoff of the peak rather
        than that of the total measurement box. After a measurement box is
        selected, the values of NC, NRX and NRY are changed to comply with
        the conventions used by mosflm. The shape of the peak as originally
        specified is maintained.
 
        Please note that it is possible that the height or width of the
        measurement box can become smaller than that of the peak. In this
        case, the size of the peak in the final measurement box is
        decreased. Use the GROW-card to fix this problem, or specify the
        minimum height or width of the measurement box to be selected.
 
        It might be necessary to rotate the measurement box 90 degrees
        if MOSFLM rotates the pattern predicted by OSCGEN because
        of the orientation in which the film was scanned. Use the YHOR
        card in this case.
 
        See the MOSFLM documentation for further information.
 
RESOLUTION x
        The resolution limit in angstrom.
 
PLOT
        Put out calculated pattern on the graphics device. In order to use
        this option with a Tektronix or Sigma terminal, before running the
        job assign the terminal to the logical file GRAPHICS and set the
        terminal to NOWRAP :
 
        $ASSIGN TT: GRAPHICS
        $SET TERM/NOWRAP
 
        To get a PLOT84 file for hard copy, assign the logical filename
        PLOT
 
        Only one PACK card can be present when plotting output on a
        terminal, but not when using PLOT84 option.
        -------------------------------------------------------------------
 
        If using TESTGEN mode, writes a file to FT04 which may then be used
        as input to CURVY to give a plot of number of overlaps vs rotation
        angle for different oscillation angles. FT04 MUST BE ASSIGNED.
        If the number of overlaps exceeds 250 it is set to 250.
 
POINT x
        The point group of the crystal. This is used in UNIQUE option
        to reduce indices to asymmetric unit of reciprocal space.
        The "member name" given below should be given:
 
                            point group            member name
 
                                1                    1
                                2                    2
                                3 (primitive)        3P
                                3 (rhombohedral)     3R
                                4                    4
                                422                  422
                                222                  222
                                32 (rhombohedral)    32R
                                23                   23
                                432                  432
                                321                  321
                                312                  312
                                6                    6
                                622                  622
 
        The required symmetry operators are read from PGDATA.LIB which
        MUST be assigned to PGIN
 
PRINT
        List all reflections (for debugging)
 
SERIAL x x x x
        The serial card can be used to specify any number of contiguous
        packs with the same oscillation range, instead of having many
        PACK cards. The four numbers to be supplied are the numbers
        of the first and the last packs, the oscillation angle, and
        the starting oscillation angle of the first pack.
        Several SERIAL cards can be given if required
 
SEPARATION x x
        The minimum separation between spot centers in the Xf
        and Yf positions on the film.  Spots closer than these limits will
        be rejected.
 
SYNCHROTRON Keywords
        Parameters that must be specified are:-
 
                WAVE   - Wavelength - Set explicity on separate card.
 
                DIVH   - Horizontal divergence of source.
 
                DIVV   - Vertical divergence of source.
 
        *****   DISPERSION - Wavelength dispersion - Set explicity on
                             separate card.
 
                DELCOR - Correlated component of wavelength dispersion.
 
        *****   MOSAIC - Mosaic spread - Set explicity on separate card.
 
        The following parameters can be set explicity by using the keywords:
 
                DIVH x
                DIVV x
                DELCOR x
 
        in any order following the 'SYNCH' keyword and using any number
        of cards. The other must be set explicity by appropriate cards.
 
        OR implicity by using keywords
 
                PX72 or PX96
 
        which will set the parameters DIVH,DIVV,DISP,DELCOR to standard
        values for PX stations for 1 dot blue collimator (0.3mm.) which are
        defined in a DATA statement.
 
***************************************************************************
 
        Following tests conducted January 1988, for data collected using
        the one dot blue collimator at Daresbury (post HBL), the following
        values are set up as defaults:
 
        Station 7.2     Horizontal divergence = 0.15 degrees
                        Vertical divergence   = 0.05
                        Dispersion            = 0.0015
                        Correlated dispersion = 0.0
 
        Station 9.6     Horizontal divergence = 0.06 degrees
                        Vertical divergence   = 0.02
                        Dispersion            = 0.0015
                        Correlated dispersion = 0.0
 
        These values, when used in conjunction with a mosaic spread of
        0.05, give good agreement with observed partial fractions in
        POSTCHK. Some crystals may well have a larger mosaic spread,
        and POSTCHK should always be used to validate the value
        assumed for mosaic spread.
 
*****************************************************************************
        The following values supplied by Helliwell and Greenhough
        ARE NO LONGER USED.
        **********************
 
        PX 9.6 station parameters for the Guinier position are:
                Vertical divergence   =  0.012 deg
                Horizontal divergence =  0.129 + ( coll. diam. mm.)* 0.29
                Conventional dispersion = 6.9E-4 +(coll. diam. mm.)* 3.5E-3
                Correlated dispersion =  0.0
 
        For 0.3 mm. collimator (1 dot blue)
                Horizontal divergence   =  0.216
                Conventional dispersion = 0.00174
 
***************************************************************************
 
TESTGEN  x x x x x
        The initial and final rotation angles for the test generation
        followed by the different oscillation angles to be tested. These
        should be supplied as the first oscillation angle to be tested, the
        final oscillation angle to be tested and the increment in oscillation
        angle to be used (eg. 0.0 90.0 2.0 3.0 0.2 will test oscillation angles
        of 2.0,2.2,2.4,2.6,2.8  and 3.0 degrees for the rotation range 0.0 to
        90.0 degrees.)
 
TITLE string
        A string of up to 80 characters.
 
UMAT x x x x x x x x x
        dimensions and the wavelength must also be specified.
        If a filename is given here, then the [U] matrix, cell parameters
        and missetting angles will be read from that file.
        This file can be output from IDXREF by using the
        OUTFILE keyword or from REFIX (written to logical filename MATRIX).
        If a subsequent CELL or MISSET keyword is given, the values
        read from the file will be superceeded. Similarly, the values
        read from the file will superceed values given on earlier CELL
        or MISSET keywords. A warning message is given in each case.
        (*** Note that this file has a total of 9 records. The first 4
        contain the [A] matrix and missetting angles, followed by
        the [U] matrix, cell parameters and missetting angles. ***)
 
UNIQUE x x x
        The starting and final rotation angle followed by the
        pack size (in degrees). The statistics produced by COMPLETE
        will be given using this pack size, eg the percentage of
        the unique data recorded as a function of total rotation
        range will be given for angular increments equal to the
        pack size. More than one UNIQUE card may be given, each card
        corresponding to a segment of data. No more than eight segments
        are allowed. If there is more than one UNIQUE card, then they
        should be supplied in order of increasing PHI angle, but this is
        not essential as the program sorts them internally. NEGATIVE PHI
        ANGLES SHOULD NOT BE GIVEN..ie -20 should be input as 340 etc.
        The only constraint on the pack size is that no more than 10000
        reflections are allowed in a pack. This will normally limit
        the pack size to a few degrees. The detail of the breakdown as a
        function of oscillation angle is of course determined by the
        pack size.
        If it is necessary to generate a list of reflections with the
        crystal in different orientations, then more than one run of OSCGEN
        will be required, and the resulting MTZ files must be sorted and merged
        using MTZUTILS. In this case it will be necessary to use the FIRSTPACK
        keyword, so that all the packs generated in different runs have
        different pack numbers. Thus if the first run generates packs 1 to 5,
        then in the second run FIRSTPACK should be 6. IT IS ESSENTIAL when
        running the program in this way that the packs are generated strictly
        in order of increasing PHI from one OSCGEN run to the next as well
        as within each run. IF THIS IS NOT DONE, THE STATISTICS PRODUCED
        BY PROGRAM 'COMPLETE' WILL BE NONSENSE. This means that
        if the same PHI range has been used for different ranges it will be
        necessary to add 360 degrees onto the specified phi angles (THIS HAS
        NOT BEEN TESTED !!!).
 
 
WAVELENGTH x
        Wavelength in Angstrom. (default is CuKalpha=1.5418)
 
YHOR
        When OSCGEN is instructed to generate a measurement box, this card
        might be necessary for a proper interfacing with MOSFLM. By default
        the measurement box is generated assuming that the X-axis of the
        predicted pattern is the horizontal axis during film measurement.
        When the YHOR card is included, the Y-axis is assumed to be
        horizontal.
 
 
 
COM FILE EXAMPLE
 
The logical file assignments are:
GENFILE   The output generate file.
PGIN    The point group library file (only used for UNIQUE option).
HKLOUT    The MTZ file output by the UNIQUE option.
PLOT      The PLOT84 or LNO3 output file for hard copy plots of the
          generated pattern.
 
********************************************************
*** To get graphical output on the terminal (PLOT keyword) do following:
$SET TERM/NOWRAP
$ASSIGN TT: GRAPHICS
********************************************************
 
$ OSCGEN GENFILE TEST.GEN
$ GO
TITLE TEST VAX MOSFLM ON 1ST 5MM AUCN FILM
IDENT CATX96
MATRIX .013216 .006608 .007513 -
 -.007199 .006322 .007188 -
 -.006901 -.013801 .006890
MISSET  0.513  0.458  3.429
LATTICE R
DIVERGENCE .35
DISTANCE 90
SEPARATION .9 .9
RASTER 23 21 9 2 2 50
FILMS 3
PACK 1 230.0 232.0
PACK 2 232.0 234.0
PACK 3 234.0 236.0
PACK 4 236.0 238.0
 
(The PACK cards could be replaced by a single SERIAL card:
SERIAL 1 4 2.0 230 )
APPENDIX
                GENERATE FILE FORMAT
                ====================
        File is direct access with record length 36 bytes
 
FILE HEADER consists of 20 records of 36 bytes. These are divided into
4 byte words which contain items listed below:
 
        Word    Contents                                        Type
 
        1-20    Title                                           char
        21-22   Crystal identifier                              char
        23-31   AMAT                                            real
        32-34   phix,phiy,phiz                                  real
        35      XTOFD  crystal to film distance                 real
        36      XMIN  ]                                         real
        37      XMAX  ]                                         real
        38      YMAX  ]   see LIMITS card in keyword input      real
        39      RMIN  ]                                         real
        40      RMAX  ]                                         real
        41      NPACK   number of packs in this file            integer
        42      MININT  minimum intensity for measurement on    integer
                        subsequent film in pack
        43      ICASS   =0 flat; =1 vee-shaped                  integer
        44      MINDTX  [ minimum separation between spots      integer
        45      MINDTY  [ in X and Y directions
        46      ISYS      type of systematic absence            integer
        47-49   KSYS(1-3) systematic absence flags              integer
        50      DSTMAX  maximum reciprocal spacing in r.l.u.    real
        51      DIVH    horizontal divergence of source         real
        52      DIVV    vertical divergence of source           real
        53      DELAMB   conventional wavelength dispersion     real
        54-59   IRAST(1-6) measurement box parameters and       integer
                           scanner stepsize
        60-62   IAX(1-3)  IAX(3) = JUMPAX                       integer
        63      LAMBDA  wavelength                              real
        64      ISYN    =0 conventional source                  integer
                        ne.0 synchrotron source
        65      ETA     mosaic spread (deg)                     real
        66      DELCOR  correlated component of wavelength
                        spread for synchrotron sources          real
        67-72   LCELL(1-6) cell parameter refinement flags      integer
        73      INOGEN  =0 conventional generate file           integer
                        =1 for 'NOGEN' file, allows separate A matrix,
                           missets and beam divergence parameters for
                           each pack
        74      IDYNAM  =0 Intensities are stored as I*2 words in
                           reflection records (film data)
                        =1 Intensities are stored as I*4 words in
                           two adjacent I*2 words in reflection
                           records (image plate data). See below.
                           This flag is set by MOSFLM, not OSCGEN.
 
PACK HEADER which is present for each pack in the file consists of 5 records
of 36 bytes: total 180 bytes.
Up to 45 4-byte words can be stored.
 
        Word    Contents                                        Type
 
        1       ID  identifier for pack                         integer
        2       NSPOT total number of spots in pack             integer
        3       NFULL  number of full spots in pack             integer
        4       PHIBEG starting 'phi' value                     real
        5       PIHEND final 'phi' value                        real
        6       NFILM  number of films in pack                  integer
        7       CCX     )                                       integer
        8       CCY     )                                       integer
        9       CCOM    ) These parameters which are determined real
        10      XTOFRA  ) from transformation refinement in     real
        11      CBAR    ) MOSFLM are written back to this file  integer
        12      ITILT   ) after processing of the 'A' film.     integer
        13      ITWIST  ) Read in for processing of 'B' and     integer
        14      IBULGE  for FLAT films only)     'C' films.     integer
        15      YSCALE  )                                       real
        16      -IBULGE  for VEE films only)                    integer
        17      +IBULGE  for VEE films only)                    integer
        18      IVERT    for VEE films only)                    integer
 
        19      CCX     )  for B film                           integer
        20      CCY     )  used in NOFID option                 integer
        21      CCOM    )                                       real
        22      CCX     )  for C film                           integer
        23      CCY     )  used in NOFID option                 integer
        24      CCOM    )                                       real
        The following are ONLY used in conjunction with the NOGEN option,
        which allows a different A matrix, missetting angles and beam
        parameters for each pack
        25-33   AMAT    A matrix for NOGEN option               real
        34-36   phix,phiy,phiz missetting angles for this pack  real
        37      ETA     mosaic spread (degrees)
        38      DIVH    horizontaldivergence (degrees)          real
        39      DIVV    vertical divergence (degrees)           real
 
REFLECTION RECORD consists of 36 bytes divided into 18 integer*2 words
 
        Word    Contents
        1       IH      )
        2       IK      ) Miller indices
        3       IL      )
        4       (IR,IM) IR - 1st byte; IM - 2nd byte
                        IR =0 reflexion is measurable
                          ne.0 reflexion failed geometrical test
                        IM =0 fully recorded
                           <0 partial recorded at start of oscillation
                           >0 partial recorded at end of oscillation
        5       IX      ) Film coordinates in 10 micron units
        6       IY      )
 
For FILM data:
        7       INTA    }
        8       ISDA    }
        9       INTB    } Intensities and standard deviations
        10      ISDB    } obtained by integration for 3 films
        11      INTC    }  in this pack
        12      ISDC    }
        13      INTPA   ]
        14      ISDPA   ]
        15      INTPB   ] Profile fitted intensities
        16      ISDPB   ] and standard deviations
        17      INTPC   ]
        18      ISDPC   ]
 
For Image plate data:
        7+8     INTA      Intensity          } For summation integration
        9       ISDA      Standard deviation }
        13+14   INTPA     Intensity          } For profile fitting
        15      ISDPA     Standard deviation }