RFCORR (CCP4: Supported Program)
                                       
NAME

   rfcorr - Analysis of correlations between cross- and self-Rotation
   functions.
   
SYNOPSIS

   rfcorr MAPIN foo.map PEAKS foo.dat
   [Keyworded input]
   
AUTHOR

   Ian Tickle, Birkbeck College, London. (tickle@cryst.bbk.ac.uk).
   
DESCRIPTION

   To analyse self- and cross-rotation function results for correlations
   between peak positions. This should help to identify firstly the
   rotational component(s) of the non-crystallographic symmetry, and
   secondly the correct peaks in the cross-rotation function. This
   requires a self-rotation function map calculated either by ALMN or by
   AMORE, i.e. the angular variables must be Eulerian, not polar (a map
   produced by POLARRFN will not work), and also a list of peaks from a
   cross-rotation function map produced by a peak search.
   
INPUT FILES

   MAPIN
          Eulerian angle self-rotation function map (at least 1
          asymmetric unit) computed by ALMN or AMORE/ROTFUN (SELF
          option).
          
   PEAKS
          Peak list of cross-rotation function map produced by ALMN or
          AMORE/ROTFUN (CROSS option). Note that if more than 50 peaks
          are given, only the first 50 are used. See ALMN keyword.
          
          Example of ALMN format:
          
PEAK  61.50      20.45     113.50  0.00000  0.00000  0.00000  9.9  0.0

          Example of AMORE format:
          
SOLUTIONRC   1      61.50      20.45     113.50  0.00000  0.00000  0.00000  9.9

          Both of these are read in free format, i.e. at least 1 space
          separating all character and numeric items.
          
KEYWORDED INPUT

   All keywords except SPACEGROUP are optional; default values are
   assumed for the others. Keywords may appear in any order, except for
   END which if present must be last. Only the first 4 characters of
   keywords are significant and all input is case-insensitive.
   
   Possible keywords are -
   
     ALMN, ANGLES, CHI, END, NUMPEAK, ORTHOG, PEAK, SPACEGROUP, TITLE
     
  TITLE <Title>
  
   Title for job (max 80 characters).
   
  ALMN
  
   Peak list assumed in ALMN format; default is AMORE format.
   
  SPACEGROUP <NSG>
  
   Space group name or number; no default. Only the rotational symmetry
   part of the space group operator is used, so lattice centring and
   translational components of screw axes are ignored. So, for example,
   P222, I222, P21212, C2221 etc. will all produce identical results.
   
  ORTHOG <NC>
  
   Orthogonalisation code used for the crystal data in ALMN or AMORE;
   default is 1.
   
  PEAK <PL>
  
   Peak limit; map values less then PL times the maximum value in the
   self-RF are not printed; default is 0.1 .
   
  NUMPEAK <NP>
  
   Maximum number of self-RF map values to print; default is 50.
   
  CHI <CHI> <TOL>
  
   Chi value to print and tolerance in degrees. This is useful for
   example to select only map values for 2-fold axes (chi = 180). Note
   that chi may be called kappa in other programs. If CHI = 0 all chi
   values > TOL are printed. The defaults are CHI = 0, TOL = 10.
   
  ANGLES <NA>
  
   Maximum number of self-RF map points for which inter-rotation axis
   angles are to be printed; default and maximum is 50.
   
  END
  
   Terminate input.
   
PRINTER OUTPUT

   The output echoes the input. Then a table of pairs of cross-RF peak
   index and symmetry index, followed by calculated polar angles theta,
   phi, chi and self-RF map value are printed sorted in descending order
   of the latter in one asymmetric unit. Note that theta may be called
   omega or psi in other programs. Finally the angles between pairs of
   rotation axis vectors, including symmetry-generated, are printed in 4
   columns.
   
EXAMPLES


set verbose
ecalc  HKLIN mrenin  HKLOUT mrenin_ecalc  <<EOD
TITLE  ** Ecalc for mouse renin crystal. **
LABI   FP=FPmrenin  SIGFP=SPmrenin
EOD

amore  HKLIN mrenin_ecalc  HKLPCK0 mrenin_ecalc.hkl  <<EOD
TITLE  ** Packing h k l E for mouse renin crystal. **
SORT
LABIN  FP=E
EOD
rm mrenin_ecalc.mtz

pdbset  XYZIN hexpep  XYZOUT hexpep_rfcell  <<EOD
SPACEG P1
CELL   80 84 97
EOD

sfall  XYZIN hexpep_rfcell  HKLOUT hexpep_rfcell <<EOD
TITLE  ** Structure factors for hexagonal pepsin in RF cell. **
MODE   SFCALC XYZIN
SFSG   1
SYMM   1
RESO   20 3
EOD

ecalc  HKLIN hexpep_rfcell  HKLOUT hexpep_ecalc  <<EOD
TITLE  ** Ecalc for hexagonal pepsin model. **
LABI   FP=FC
EOD

amore  HKLIN hexpep_ecalc  HKLPCK0 hexpep_ecalc.hkl  <<EOD
TITLE  ** Packing h k l E for hexagonal pepsin model. **
SORT
LABIN  FP=E
EOD
rm hexpep_rfcell.mtz hexpep_ecalc.mtz

amore  HKLPCK0 mrenin_ecalc.hkl  HKLPCK1 hexpep_ecalc.hkl  \
       CLMN0 mrenin.clmn  CLMN1 hexpep.clmn  MAPOUT mrenin_cross  \
       >! mrenin_cross.log  <<EOD
ROTFUN
TITLE  ** Cross rotation function with E's. **
CLMN   CRYST  ORTH 3  RESO 20 3  SPHERE 35
CLMN   MODEL 1  RESO 20 3  SPHERE 35
ROTATE CROSS  MODEL 1  NPIC 20
EOD
rm mrenin_cross.map

amore  HKLPCK0 mrenin_ecalc.hkl  CLMN0 mrenin.clmn  \
       MAPOUT mrenin_self  <<EOD
ROTFUN
TITLE  ** Self rotation function with E's. **
ROTATE SELF  NPIC 20
EOD

grep SOLUTIONRC mrenin_cross.log >! mrenin_cross.dat

rfcorr MAPIN mrenin_self  PEAKS mrenin_cross.dat  <<EOD
TITLE  ** Mouse renin self/cross rotation function correlation. **
SPACEG p2
ORTH   3
CHI    180
EOD

   The output below shows the 222 non-crystallographic symmetry. The
   first table echos the 8 input peaks from the cross-rotation function.
   The second table shows the positions of the 10 points in the
   self-rotation function above the default threshold corresponding to
   the non-crystallographic 2-fold axes (chi ~= 180) that relate pairs of
   the highest 4 peaks, including symmetry related, in the cross-RF. The
   last table shows the ~90 deg angles between these points in the
   self-RF.

  Peak     Alpha      Beta     Gamma

     1     61.50     20.02    113.50
     2     68.33     26.06    107.24
     3    112.50    154.69    289.00
     4    116.00    157.55    293.50
     5    103.14     88.09    166.45
     6     70.12    116.85     97.56
     7     67.00    105.43     97.30
     8    114.90      8.17    100.72



 Serial   #Peak   #Peak(#Symm)      Theta    Phi    Chi   self-RF

      1       3       4 ( 2)            2     81    179     78.75
      2       1       2 ( 2)            3     87    179     51.59
      3       2       3 ( 2)           90    180    179     39.46
      4       2       3 ( 1)           90     90    180     39.46
      5       1       3 ( 2)           90    179    174     37.41
      6       1       3 ( 1)           87     89    179     37.41
      7       1       4 ( 1)           89     89    179     32.41
      8       1       4 ( 2)           89    179    178     32.41
      9       2       4 ( 2)           90    179    176     25.68
     10       2       4 ( 1)           88     89    179     25.68



 Inter-vector angles: Serial[i]  Serial[j] (Symm[j])  Angle, in 4 columns.

    1   2( 1)    2      1   2( 2)    5      1   3( 1)   90      1   3( 2)   90
    1   4( 1)   88      1   4( 2)   89      1   5( 1)   90      1   5( 2)   89
    1   6( 1)   89      1   6( 2)   86      1   7( 1)   89      1   7( 2)   87
    1   8( 1)   90      1   8( 2)   89      1   9( 1)   90      1   9( 2)   89
    1  10( 1)   86      1  10( 2)   90      2   3( 1)   90      2   3( 2)   90
    2   4( 1)   86      2   4( 2)   87      2   5( 1)   90      2   5( 2)   90
    2   6( 1)   90      2   6( 2)   84      2   7( 1)   88      2   7( 2)   86
    2   8( 1)   90      2   8( 2)   89      2   9( 1)   90      2   9( 2)   89
    2  10( 1)   85      2  10( 2)   89      3   4( 1)   90      3   4( 2)   90
    3   5( 1)    1      3   5( 2)    1      3   6( 1)   89      3   6( 2)   89
    3   7( 1)   89      3   7( 2)   89      3   8( 1)    1      3   8( 2)    1
    3   9( 1)    0      3   9( 2)    1      3  10( 1)   90      3  10( 2)   90
    4   5( 1)   89      4   5( 2)   89      4   6( 1)    3      4   6( 2)    2
    4   7( 1)    2      4   7( 2)    1      4   8( 1)   89      4   8( 2)   89
    4   9( 1)   90      4   9( 2)   90      4  10( 1)    2      4  10( 2)    3
    5   6( 1)   90      5   6( 2)   90      5   7( 1)   90      5   7( 2)   90
    5   8( 1)    0      5   8( 2)    1      5   9( 1)    0      5   9( 2)    1
    5  10( 1)   90      5  10( 2)   90      6   7( 1)    2      6   7( 2)    4
    6   8( 1)   90      6   8( 2)   90      6   9( 1)   90      6   9( 2)   90
    6  10( 1)    5      6  10( 2)    1      7   8( 1)   90      7   8( 2)   90
    7   9( 1)   89      7   9( 2)   89      7  10( 1)    3      7  10( 2)    1
    8   9( 1)    1      8   9( 2)    1      8  10( 1)   89      8  10( 2)   89
    9  10( 1)   90      9  10( 2)   90

SEE ALSO

   Calculation of rotation function:
     * almn
     * amore