TFFC (CCP4: Supported Program)
                                       
NAME

   tffc - Translation Function Fourier Coefficients
   
SYNOPSIS

   tffc hklin foo_in.mtz hklout foo_out.mtz
   [Keyworded input]
   
DESCRIPTION

   TFFC is a full-symmetry Translation Function program based on the
   Harada, Lifchitz, Berthou and Jolles formulation of the Crowther and
   Blow T2 function, and it can also be used to calculate the TO/O
   function of Harada et al. TFFC uses structure factor information
   (amplitudes and phases) from all molecules in the unit cell whose
   positions have already been determined by previous runs of the
   program, or are about to be determined in the current run, and not
   merely pairs of molecules, as does the C & B T1 function.
   
   Amplitude-only information from all molecules of known orientation in
   the unit cell, including any not related by crystallographic symmetry
   (whose positions are consequently unknown), is however used in the
   Fobs/Fcalc scaling, in the calculation of normalised structure factor
   amplitudes, and optionally in the subtraction of the transform of the
   intramolecular vector set.
   
   The conventional crystallographic T2 function is in general the
   3-dimensional sum function of the pairwise 2-dimensional T1 functions;
   however in polar space groups the crystallographic T2 function is also
   2-dimensional. It is especially advantageous in high-symmetry space
   groups, where the smaller signal/noise ratio of the peaks in the T1
   functions may cause difficulties.
   
   TFFC works for all space-group symmetries containing only rotation and
   screw axes, and non-primitive lattice elements, provided the
   conventional settings in International Tables Vol. A are used (R3 must
   be indexed on hexagonal axes).
   
   The partial T2 function (also called non-crystallographic, meaning
   obtained using structure factors from a partially known structure,
   which may or may not be related by non-crystallographic symmetry to
   the remaining unknown part) is also the 3-dimensional sum function of
   the pairwise partial T1 functions; however the partial T1 and T2
   functions are always 3-dimensional. The program can also be used to
   calculate the individual T1 functions, but a satisfactory automatic
   method for analysing these functions has yet to be devised, and so
   they have to be analysed manually (hopefully this should never be
   necessary!).
   
   The T2 Translation Function can be used to resolve a space group
   ambiguity, for example, I222/I212121 or P3121/P3221, where the
   systematic absence conditions do not distinguish the pairs, or for
   example P21212/P212121 where the identification of systematic absences
   is not always clear-cut.
   
   Three important features which further improve the signal/noise ratio
   of the T2 function are the shell-scaling of the F(obs) and F(calc)
   values by the difference Wilson method, the use of normalised
   amplitudes (E values), and the subtraction of the transform of the
   intramolecular vector set from the transform of the Patterson function
   of the target structure.
   
   The program works by calculating the Fourier coefficients of the
   Translation Function from the transform of the intermolecular vector
   set, and the Fast Fourier Transform (FFT) program is used to effect
   the transformation into real space. This method is about 3 orders of
   magnitude faster than a real space search, and the speed is also much
   less dependent on the fineness of the grid search.
   
PRE- AND POST-PROCESSING REQUIREMENTS

   It is assumed that the Rotation Function (e.g. program AMORE) has been
   used to get an accurate orientation (within 2.5 deg at 3 Angstrom
   resolution) of the model structure (preferably with thermal
   parameters) to the maximum resolution of the data available. All
   structure factors to this resolution for one asymmetric unit in space
   group P1 in the cell of the target structure are required (program
   SFALL). Then the calculated structure factors are combined with the
   observed amplitudes (program CAD); for each hkl there will be one Fobs
   with sigma(Fobs) and a number (equal to the number of asymmetric units
   in the primitive unit cell of the unknown structure) of Fcalc values
   with PHIcalc.
   
   IMPORTANT: The unit cell specified in SFALL must be the experimentally
   determined cell of the crystal whose structure is being determined,
   not some arbitrarily chosen cell as in the Rotation Function. This is
   because the aim is to match the inter-molecular vectors (not the
   intra-molecular ones). This is clearly not possible if the cells of
   the unknown and model structures are different.
   
   If there is more than one molecule per asymmetric unit then the above
   procedure must be repeated for each molecule, using column labels of
   the form FCA1 PCA1 FCA2 PCA2 ... for the first molecule, FCB1 PCB1
   FCB2 PCB2 ... for the second and so on. The files must then be
   column-merged into a single input reflection file (using CAD this
   operation can be done in a single run).
   
   The output of TFFC is used as input to the P1 version of FFT. The
   program outputs two sets of Fourier coefficients; for the TO/O
   function two FFTs are necessary, using labels A and B for the TO
   function and AO and BO for the O function. It is not necessary to
   print any maps; instead specify binary map output in FFT and use the
   program MAPSIG to perform the division TO/O and analyse the results.
   For the T2 function only the labels A and B are used, only one FFT is
   done, but MAPSIG can still be used.
   
   When computing the TO and O functions, the F000 terms must be entered
   manually into the FFT program; the required values are given at the
   end of the TFFC printer output (the two values are for the TO and O
   functions respectively). The volume V must also be given, but this
   acts only as an arbitrary scale, and any value (typically around 1000)
   which gives sensible magnitudes in the Translation Function map can be
   used.
   
   Note that the reflection indices produced by TFFC are not the same as
   those read from the input reflection file. Consequently the S values
   calculated for these reflections are meaningless, and therefore it is
   important not to apply any resolution cutoffs in FFT. If resolution
   cutoffs are desired they must be applied by TFFC to the original
   indices.
   
KEYWORDED INPUT

   Data are introduced by the following keywords:
   
     FIND, LABIN, LIST, NONCRYST, PART, POINTGROUP, RESOLUTION, SELF,
     SHELL, SPACEGROUP, SYMMETRY, TITLE, VECTOR.
     
   Only the first 4 characters of each keyword are significant. All
   keywords are optional, though normally one would specify LABIN to use
   other than the default file labels.
   
   The keywords SPACEGROUP and SYMMETRY are mutually exclusive; one or
   the other is only required if the space group information in the
   reflection file header is incorrect. This may happen because the
   systematic absences do not unambiguously define the space group; the
   point group information defined by the rotation components of the
   symmetry matrices however must be correct. It is not then necessary to
   re-run SFALL & CAD, it is only necessary to specify the correct
   symmetry with either SPACEGROUP or SYMMETRY.
   
VERY IMPORTANT

   The SPACEGROUP option can only be used if:
    1. Phase shifts due to any screw-axis translations have not already
       been applied, and
    2. The primitive General Equivalent Positions in symop.lib are in
       exactly the same order as those used when the input reflection
       file was prepared.
       
   If the space group has screw-axis translations (ignoring non-primitive
   lattice translations), and an earlier program used the translation
   components to apply phase shifts, the SPACEGROUP option cannot be
   used. The SYMMETRY option must be used and the screw-axis translations
   then omitted.
   
   The SYMMETRY option must also be used if the primitive General
   Equivalent Positions in symop.lib are in a different order from those
   originally specified. This can happen either because for some space
   groups different editions of International Tables have the equivalent
   positions in a different order, or because for some space groups with
   the same point group, the order of the rotation components may vary.
   When the SYMMETRY option is used, the order of equivalent positions
   must be identical with that used when the input file was prepared.
   
   No problems should occur using the SPACEGROUP option if
    1. the current versions of the SFALL and CAD programs have been used,
       and
    2. the current version of symop.lib has been used consistently.
       
DESCRIPTION OF KEYWORDS

  TITLE [String]
  
   Title (default is to use reflection file title).
   
  SPACEGROUP [String or Integer]
  
   Name (as in symop.lib) or number in International Tables.
   
  POINTGROUP [String or Integer]
  
   Name (optionally beginning with pg). This must be one of the following
   :

   1    2  222    3  312  321    4  422    6  622   23  432

The number of primitive g.e.p.'s to follow must be then :

   1    2    4    3    6    6    4    8    6   12   12   24

   The default is to use the point group implied by the space group. The
   space/point group may be 1 (one equivalent position) only if the PART
   option is specified.
   
  SYMMETRY [String]
  
   Primitive general equivalent position(s) in same format as
   International Tables, with one or more per line, separated by * and/or
   repeating keyword where necessary. In whatever way the g.e.p.'s are
   set up (SPACEGROUP or SYMMETRY), they must exactly correspond in order
   to those used to generate the input reflection file.
   
  NONCRYST [Integer]
  
   Number of non-crystallographic subunits per crystallographic
   asymmetric unit; must be between 0 and 8 inclusive. The default is one
   molecule per asymmetric unit; this is also implied by values of 0 or
   1.
   
  SELF
  
   Intramolecular vector contributions are included. This is required for
   the TO/O function. The T2 function is the default (intramolecular
   vector set subtracted).
   
  SHELL [Integer]
  
   Approximate number of reflections per shell to divide data for scaling
   (default = 100). This value will be reset if the number of shells is
   more than 200. The program will stop with an error message if any
   shell is empty; the number of reflections per shell should then be
   increased.
   
  RESOLUTION [Real(2)]
  
   Resolution limits (d-spacings in Angstrom) to be applied (either way
   round); the default is 20 0 and these values are recommended for the
   initial run.
   
  LIST [Integer]
  
   Number of reflections to list (default = 0). This is only useful for
   debugging.
   
  VECTOR [String] [Real(3)]
  
   In the case of non-crystallographic symmetry, this is specified for
   each subunit (A, B, C ... H) whose fractional translation vector (Tx,
   Ty, Tz) has been determined by a previous run of TFFC, or otherwise.
   
  FIND [String]
  
   In the case of non-crystallographic symmetry, this is specified for
   the subunit (A, B, C ... H) whose translation is to be determined in
   this run. There may be only one FIND, but it may be omitted if all but
   one subunit translations have been defined using VECTOR.
   
  PART
  
   This sets up the calculation of the partial (non-crystallographic)
   Translation Function (previously done by program TFPART). The default
   is to calculate the crystallographic Translation Function (previously
   program TFSGEN).
   
   With this option NONCRYSTVECTOR
   . For example if NONCRYST is given as 4, then 3 runs of the program
   would be required:

Run 1 :  VECTOR  A  Ax Ay Az
         FIND    B

Run 2 :  VECTOR  A  Ax Ay Az
         VECTOR  B  Bx By Bz
         FIND    C

Run 3 :  VECTOR  A  Ax Ay Az
         VECTOR  B  Bx By Bz
         VECTOR  C  Cx Cy Cz
         FIND    D

   The first translation vector for the A subunit could be determined by
   the crystallographic Translation Function, except in P1 where the
   first translation vector can be chosen arbitrarily. Note that the
   translations need not be determined in the order shown; it may be
   easier to start by fixing one of the other subunits, and then
   determine the other translations in a different order.
   
   To calculate a T1 function, both the subunit label and the number of
   the equivalent position must be specified in VECTOR (of which there
   may only be one) and FIND; for example:

VECTOR  A1  Ax Ay Az
FIND    B2

  LABIN [String]
  
   MTZ column label assignments.
   
   If NONCRYST = 0 or omitted, the program labels are:

H K L FP SIGFP FC1 PC1 FC2 PC2 ...

where FP, SIGFP = Fobs, sigma(Fobs)
FCn, PCn = Fcalc and phase of n'th asymmetric unit of model.

   If NONCRYST > 0 the program labels are H K L FP SIGFP (Fobs,
   sigma(Fobs)), followed by NONCRYST*NUMGEP pairs of columns containing
   the partial Fcalc, phase contributions (NUMGEP = number of primitive
   g.e.p.'s).
   
   For example, if NONCRYST = 4, NUMGEP = 2, the column labels would be:

       FCA1  PCA1  FCA2  PCA2  FCB1  PCB1  FCB2  PCB2
       FCC1  PCC1  FCC2  PCC2  FCD1  PCD1  FCD2  PCD2

   i.e. the letters A,B,C,D refer to non-crystallographically related
   subunits and the numbers 1,2... refer to crystallographically related
   subunits.
   
NOTES

  The asymmetric unit of the crystallographic Translation Function
  
   The Translation Function is always computed in space group P1, but in
   many cases the crystallographic T function has extra translational
   symmetry, due to the presence of equivalent origins in the space
   group, which reduces the size of the asymmetric unit which need be
   computed. These alternative origins arise either from rotational
   symmetry elements or from non-primitive lattice translations. The
   Translation Function never has rotational symmetry. However it should
   be approximately centrosymmetric about the solution vector, but since
   this is unknown, and therefore in a general position, this information
   cannot be used to reduce the size of the asymmetric unit.
   
   In polar space groups, the translation vector for the crystallographic
   T function is limited to the plane perpendicular to the unique axis,
   so only one section need be calculated; also, all space groups have
   equivalent origins, which reduces the asymmetric unit of the
   Translation Function, e.g. in orthorhombic, these origin positions are
   at 0 and 1/2 in x, y and z, which reduces the asymmetric unit to 0 to
   1/2 along each axis. The table below shows the asymmetric unit for
   each point group.
   
   Monoclinic
   (b unique) pg2:   y=0 section, 0 to 1/2 along x and z.
   
   Orthorhombic pg222:   0 to 1/2 along x, y and z.
   
   Trigonal pg3:   z=0 section, 0 to 1 along x and y.
   pg312 and pg321:   0 to 1 along x and y, 0 to 1/2 along z.
   
   Note that in trigonal point groups it is not possible to calculate
   just one asymmetric unit by applying limits parallel to the cell
   edges. Consequently the ranges suggested actually enclose 3 equivalent
   origins.
   
   Tetragonal pg4:   z=0 section, 0 to 1 along x,
   0 to 1/2 along y (or vice versa).
   pg422:   x and y as for pg4, 0 to 1/2 along z.
   
   Hexagonal pg6:   z=0 section, 0 to 1 along x and y.
   pg622:   0 to 1 along x and y, 0 to 1/2 along z.
   
   Cubic pg23/pg432:   0 to 1/2 along x, 0 to 1 along y and z
   (or any other permutation).
   
   In centred space groups, these asymmetric units may be reduced
   further. Note that although higher symmetry point groups have smaller
   asymmetric units (as a fraction of the unit cell) in the space group,
   they have larger asymmetric units in the Translation Function.
   
  The asymmetric unit of the partial Translation Function
  
   The partial Translation Function only has translational symmetry
   arising from the lattice-centring symmetry elements, so that for all
   primitive space groups regardless of the point group symmetry, a
   complete unit cell in P1 must be computed. For centred cells this can
   be reduced; for I-centred cells, for example, 1/2 a cell must be
   computed.
   
  Combining the crystallographic and partial Translation Functions
  
   If TFFC is used in the presence of non-crystallographic symmetry, it
   must be given the partial structure factors of all the subunits of
   known orientation, whether the translations of the subunits are known
   or not. The crystallographic and partial Translation Functions are
   then calculated separately; of course the partial T function cannot be
   calculated unless at least one translation vector has been determined
   using the crystallographic T function (or in the case of space group
   P1, the first vector can be fixed arbitrarily).
   
   For a given subunit, the total Translation Function is simply the sum
   of crystallographic and partial contributions, and the program MAPSIG
   can be used to do this summation (a minimum function could be used,
   but I have not tried this). In practice I have not found it necessary
   to do this summation; manual inspection of the peak lists generated
   from the separate maps is usually all that is necessary.
   
INPUT AND OUTPUT FILES

  Input files
  
   Unit 5
          The input control data.
          
   HKLIN
          The input reflection data in standard CCP4 format.
          
  Output files
  
   Unit 6
          The line printer output.
          
   HKLOUT
          The output reflection data in standard CCP4 format.
          
  Reflection output file labels:
  
   H K L A B AO BO
   
   The A and B columns (real and imaginary components of the Fourier
   coefficient of the transform of the Translation Function) are used in
   a run of FFT in P1. The solution vector should appear as a single
   peak; the corresponding molecule is to be translated by this vector.
   The AO and BO columns are the transform of the Harada et al O
   (overlap) function.
   
PROGRAM STRUCTURE

   The TFFC program is a merger of the Translation Function programs
   TFSGEN and TFPART, with the PART option added to select the
   appropriate code. The program consists of the following routines:
   
   TFFC (main subprogram)
   Dimensions a working array (not used when PART option is selected).
   Calls CCPFYP and TFMAIN.
   
   BLOCK DATA
   Initialises file titles,flags for Harker section test, sums for
   scaling.
   
   TFMAIN
   Calls GETINP to set up input data, calls GENPGT (for partial T1
   function only), reads MTZ file first time for resolution range, reads
   MTZ file second time for scale factor sums, putting Fobs^2 and Fcalc^2
   into bins of constant d*^3, calculates maximum indices and scale
   factors. For crystallographic T function dimensions a number of
   complex arrays (one for each Harker section) and calls TFSGEN. For
   partial T function calls TFPART.
   
   GETINP
   Calls MTZINI, opens HKLIN reflection file. Calls PARSER to read
   control data and checks it. Sets up input labels and calls GRASSN to
   do input file assignments.
   
   GRASSN
   Makes input MTZ file assignments.
   
   GENPGT
   Generates point group multiplication table.
   
   MULEPS
   Calculates reflection multiplicity and symmetry weight factor epsilon.
   
   GENEQ
   Generates equivalent reflection.
   
   TFSGEN
   Reads MTZ file third time, applies scales using spline interpolation
   (FSPLIN). Accumulates translation and overlap Fourier coefficients in
   arrays. This is necessary because the FFT input routines only use the
   last coefficients read in for a particular hkl (to avoid having to
   worry about reflection multiplicity). Calls GWOPEN to open output MTZ
   file HKLOUT and writes structure factors using routine PUTREF.
   
   FSPLIN
   Cubic spline interpolation.
   
   GWOPEN
   General purpose output file (HKLOUT) open for MTZ.
   
   PUTREF
   Writes a structure factor to HKLOUT, accumulating minimum, maximum and
   sum statistics for data columns.
   
   TFPART
   Calls GWOPEN to open output MTZ file HKLOUT. Reads MTZ file third
   time, applies scales using spline interpolation (FSPLIN). Calculates
   translation and overlap Fourier coefficients and writes structure
   factors using routine PUTREF.
   
IMPLEMENTATION

   For large problems it may be necessary to increase the dimension of
   the large array A. If this is required, an appropriate message will be
   issued; change the array dimension in the first PARAMETER statement
   (NA), then re-compile and re-link.
   
EXAMPLES

  Crystallographic Translation Function for structure with only
  crystallographic symmetry
  
#
tffc hklin tffc_inp hklout tffc_out << eof
TITL test TFFC  P6522 hex pepsin.
SPAC P6522
LABI FP=FOHEXPEP SIGFP=SIGHEXPEP
eof
#
fft hklin tffc_out mapout tffc_out << eof
LABI A=A B=B
TITL T2 function for hex pepsin assuming P6522.
AXIS Y,X,Z
GRID 72 72 300
XYZL 0 1 0 1 0 .5
VF00 1000
eof
#
mapsig mapin tffc_out  << eof
eof
#

  Crystallographic Translation Function in the presence of non-crystallographic
  symmetry or partial structure
  
#
tffc  hklin bbp_tf  hklout tffc_out  << eof
TITL  C222 Find subunit B1 using A1 known.
SPAC  C222
SHEL  150
NONC  2
VECT  A 0.491 0.224 -0.002
LABI  FP=FO SIGFP=SIGFO -
      FCA1=F1B1 PCA1=PC1B1 FCA2=F1B2 PCA2=PC1B2 -
      FCA3=F1B3 PCA3=PC1B3 FCA4=F1B4 PCA4=PC1B4 -
      FCB1=F2B1 PCB1=PC2B1 FCB2=F2B2 PCB2=PC2B2 -
      FCB3=F2B3 PCB3=PC2B3 FCB4=F2B4 PCB4=PC2B4
eof
#
fft   hklin tffc_out  mapout tffc_out  << eof
LABI  A=A B=B
TITL  C222 Find subunit B1 using A1 known.
AXIS  Y,X,Z
VF00  1000
GRID  192 208 96
XYZL  0 .5  0 .5  0 .5
eof
#
mapsig  mapin tffc_out  << eof
eof
#

  Partial Translation Function
  
#
tffc  hklin bbp_tf  hklout tffc_out  << eof
TITL  C222 Find subunit B1 using A1 known.
SPAC  C222
SHEL  150
NONC  2
VECT  A 0.491 0.224 -0.002
PART
LABI  FP=FO SIGFP=SIGFO -
      FCA1=F1B1 PCA1=PC1B1 FCA2=F1B2 PCA2=PC1B2 -
      FCA3=F1B3 PCA3=PC1B3 FCA4=F1B4 PCA4=PC1B4 -
      FCB1=F2B1 PCB1=PC2B1 FCB2=F2B2 PCB2=PC2B2 -
      FCB3=F2B3 PCB3=PC2B3 FCB4=F2B4 PCB4=PC2B4
eof
#
fft   hklin tffc_out  mapout tffc_out  << eof
LABI  A=A B=B
TITL  C222 (T2):find translation vector for molecule 1B using 1A known
VF00  1000
GRID  192 208 96
XYZL  0 1 0 .5 0 1
eof
#
mapsig  mapin tffc_out  << eof
eof
#

  Example to find second non-crystallographic translation symmetry
  
#!/bin/csh -f
#   Calculate Translation Function (TFFC),
#   Map (FFT) and find peaks (PEAKMAX)
#
#  goto FFT
#  goto PEAKMAX
#  goto PLUTO
#
TFFC:
#
tffc  hklin  ../mtz/i96v/cad_all2.mtz
      hklout ../mtz/i96v/tf_all2.mtz
             << eof
TITL Barnase finding B1, A1 known
POINTGROUP pg3
SYMMETRY  X,Y,Z * -Y,X-Y,Z * Y-X,-X,Z
SHEL 150
NONC 3
VECT A 0.690 0.865 0.000
FIND B
PART
LABI FP=iv96_F    SIGFP=iv96_SIGF -
     FCA1=FCP_A1   FCB1=FCP_B1     FCC1=FCP_C1   -
     PCA1=PHICP_A1 PCB1=PHICP_B1   PCC1=PHICP_C1 -
     FCA2=FCP_A2   FCB2=FCP_B2     FCC2=FCP_C2   -
     PCA2=PHICP_A2 PCB2=PHICP_B2   PCC2=PHICP_C2 -
     FCA3=FCP_A3   FCB3=FCP_B3     FCC3=FCP_C3   -
     PCA3=PHICP_A3 PCB3=PHICP_B3   PCC3=PHICP_C3
eof
#
exit
#
#   Make a map with FFT, find peaks with PEAKMAX
#
FFT:
#
fft  hklin ../mtz/i96v/tf_all2.mtz
     mapout map/tf_all2.map
     <<  eof
RESO 100 1
LABIN A=A B=B
TITLE TF all for C from ALMN ---> TFFC
!SCALE Label Scale B-factor                      ! optional
!NOCHECKS                                        ! optional
!SYMMETRY 1         !space-group name or number  ! optional
!FFTSYMMETRY 1      !space-group name or number  ! optional
AXIS Z X Y          !Axis order fast, medium, slow
GRID 200 200 200    !nx ny nz
VF000 0 145300
XYZLIM 0 1 0 1 0 1  !xmin xmax ymin ymax zmin
!BIAS bias [optional]
!EXCLUDE keyword1 value1 keyword2 value2 .
!PROJECTION                                      !optional
!RHOLIM rhomax [rhomin]                          !optional
eof
#
PEAKMAX:
#
peakmax  mapin map/tf_all2.map
         to    peaks/tf_all2.peaks
         << eof
output peaks
threshold rms 3
numpeaks 20
eof
#
exit
#
NPO:
npo mapin  map/tf_all.map
      plot   tf_all.plt
      << eof
TITL Translation function, solution 2 from TFFC
MAP
CONTRS 1 TO 6  BY .08
SECTNS 0
PLOT
eof
#
xplot84driver tf_all.plt
#
exit
#

AUTHOR

   Ian Tickle, Birkbeck College.
   
SEE ALSO

   amore, sfall, cad, fft, mapsig (1)
   
REFERENCES

    1. Molecular Replacement, Proceedings of the Daresbury Study Weekend,
       (1985) DL/SCI/R23
    2. Molecular Replacement, Proceedings of the Daresbury Study Weekend,
       (1992) DL/SCI/R33